## Slide 1: Constructing Boolean Algebras
Gayan Rukshantha gayanp@nsbm.lk
Lecturer
Faculty of Computing
NSBM Green University

## Slide 2: The Truth Table
An automated cooling system consist with three sensors X, Y, Z. The system automatically turns ON (1/True) and OFF (0/False) when following conditions apply from the three sensors.
X | Y | Z | System
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 3: Mintems & Maxterms
Minterms –
Represents exactly one combination in the truth table.
Denoted by mj, where j is the decimal equivalent of the minterm’s corresponding binary combination (bj).
A variable in mj is complemented if its value in bj is 0, otherwise is uncomplemented
Maxterms –
Represents exactly one combination in the truth table.
Denoted by Mj, where j is the decimal equivalent of the maxterm’s corresponding binary combination (bj).
A variable in Mj is complemented if its value in bj is 1, otherwise is uncomplemented.

## Slide 4: Mintems & Maxterms
X | Y | Z | System
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 5
In a simple copy machine, a stop signal, S, is to be generated to stop the machine operation and energize an indicator light whenever either of the following conditions exists:
(1) there is no paper in the paper feeder tray; or (2) the two microswitches in the paper path are activated, indicating a jam in the paper path. The presence of paper in the feeder tray is indicated by a HIGH at logic signal P. Each of the microswitches produces a logic signal (Q and R) that goes HIGH whenever paper is passing over the switch to activate it.
Design the logic circuit to produce a HIGH at output signal S for the stated conditions, and implement it using the 74HC00 CMOS quad two-input NAND chip.

## Slide 6: Standard Forms
There are two types of Standard Forms
  Sum Of Products
  Products of Sum

## Slide 7: Sum of Products
Simplifying Boolean Expressions using Graphical Approach

## Slide 8: Product of Sum
X | Y | Z | System | Term
0 | 0 | 0 | 0 | Minterm
0 | 0 | 1 | 0 | Minterm
0 | 1 | 0 | 1 | Maxterm
0 | 1 | 1 | 0 | Minterm
1 | 0 | 0 | 1 | Maxterm
1 | 0 | 1 | 1 | Maxterm
1 | 1 | 0 | 0 | Minterm
1 | 1 | 1 | 1 | Maxterm

## Slide 10: Products of Sum

## Slide 11: Thank You !!